## Slide 1
Remove 2 hex screws (3/16 allen wrench)
3/16th hex screws

## Slide 2
Use friction of palm to pull up the plastic cover. Remove both covers.
It requires a lot of force.

## Slide 3
Internals. Remove everything except cables in the next slides.
Remove back panel.
Remove brackets/covers (red arrow) if needed.
RACs
Bracket
Cover
“Shoulders”
Back panels
“SJA2”
PSM2
“SJX”
PSM3
“SJC”
ECM
“SJA1”
PSM1

## Slide 4
Unplug and preserve the cable labeled “Z-AXIS”. Squeeze the tab and pull.
Plug it into “Z axis” connector in a dESSJ. This dESSJ does not need any other connection except for USB power.
“Z-AXIS”
Preserve

## Slide 5
Pay attention to the 4 RACs (red arrow). Carefully unplug and label cables from them. See next slide.
Make sure you know which RAC the cables are unplugged from. bundle and label them with the name of the arm. Some of the cables already have labels on them. See left image for mapping to robot arm names.
From each RAC, you should get
a large bundle of cables with 3 white rectangular connector + 1 “firewire” connector + 1 grounding wire with ring terminal, and
a small 2-wire cable with a white rectangular connector. Keep track of which RAC/arm this cable belongs to.

## Slide 6
Unplug and preserve cables from RAC. No need to label individual cables. They are all different.
3x in the front
1x ring terminal on the top
1x “firewire” in the back. J11. Remove RAC from the giant sheet metal plate before unplugging this cable to avoid damage to the connector.
SJA2 bundle from column
2-wire cable
Ground ring connector
FireWire LVDS on J11

## Slide 7
Plug the cables into dSIB-Si
Preserve
SJA2 RAC
PSM2 dSIB

## Slide 8
Stack the controllers in the gutted SUJ. Plug in the dSIB-Si

## Slide 9
On the SUJ arms, remove ESSJ (red arrow, 4 places).
Replace with dESSJ and plug in cables.
ESSJ
dESSJ
LVDS
Power
Potentiometers (3 except ECM: 4)